Toyota Celica ST185 GT4 Carlos Sainz ECU Pinout

| E01 | Power Ground | RSC | ISC Valve | RLY | Relay? |
| --- | --- | --- | --- | --- | --- |
| E02 | Power Ground | INT | Intercooler ECU | TVIS | Intake Air VSV |
| No.1 | Injector | HT | O2 Sensor Heater | E1 | Engine Ground |
| No.2 | Injector | STJ | Cold Start Injector |  |  |
| No.3 | Injector | IGT | Igniter EGR EGR VSV |  |  |
| No.4 | Injector | G2 | Distributor |  |  |
|  |  | G1 | Distributor |  |  |
|  |  | NE | Distributor |  |  |
|  |  | G | Distributor |  |  |
|  |  | IGF | Igniter TPC Turbo Pressure VSV |  |  |
|  |  | RSO | ISC Valve |  |  |

| VF | Check Connector | PIM | Turbo Pressure Sensor | THA | THA Air Temp Sensor | E2 | Sensor Ground |
| --- | --- | --- | --- | --- | --- | --- | --- |
| TE1 | Check Connector | KNK | Knock Sensor | VTA | VTA Throttle Posn Sensor |  |  |
| TE2 | Check Connector | THW | Water Temp Sensor | VS | VS Air Flow Meter |  |  |
| OX | Check Connector | IDL | Throttle Position Sensor | VC | VC Sensor Power Source |  |  |

| STA | Starter Switch | ATS | ??? | WIN | Intercooler ECU | Batt | Battery |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ACT | A/C Amplifier | FPR | Fuel Pump Relay | FC | Circuit Opening Relay | +B1 | Main Relay |
| AC | A/C Magnet Switch | W | Warning Light | ELS | Taillight and Defogger | +B | Main Relay |
| SPD | Speed Sensor | STP | Stop Light Switch |  |  |  |  |